## Slide 1: Lumerical Learning Process

## Slide 2: Starting With The Basics (MODE)
Starting with the GUI
  Learn how to create structures
    Define geometry
    Define material
  Learn how to create sources + ports
    Define each type
      I.e. Mode
      I.e. Frequency Domain

## Slide 3: First Waveguide!!!

## Slide 4: Learned Procedure
Define structure
Define inputs + outputs
Simulate and find s-parameters

## Slide 5: Learning Layer Builder
Use .gds to define 2D layout structure
Use .lsf to define object
  Including Layer builder
    General structures (waveguide, rectangle, monitors, etc)
Running
  Either in Lumerical GUI
  Or scripting in python and calling the lumapi

## Slide 6: Building Our First Curved Waveguide
Procedure
  Create a .gds file with python
    Generate a sequence of points
    Combine to form a polygon and export to .gds format
  View with klayout
  Import .gds into the .lsf
  Use .lsf to generate the layout builder object and help to simulate performance

## Slide 8: Simulating Performance Of Our First Waveguide
Procedure
  Add ports + monitors
    In the .lsf add the objects
  Add the FDTD region + mesh
  Run procedure + performance metric display

## Slide 10: Simulating Performance Of Our First Waveguide
Results!!!
  Loss
    5 dB!!!
We start improving from here

## Slide 11: Generating our First Material (LN)
Just add to the material database/catalogue

## Slide 12: Performing Our First Optimization
Rough idea
  Use Lumopt to optimize several segments of the waveguide bend
    We used 8 segments of varying radii and optimized for the best combination of them
Result
  The simulated connections between the different segments were not handled well as a result the best combination turned out to be the same seeded value (smoothed 25 um radius)
  Loss maintained at 5 dB

## Slide 13: Performing Our First Optimization
Learning
  We need to design a better approach for the waveguide design before optimization such that the parameters work

## Slide 14: Code
In the notes
Notes: import sys
import os
import numpy as np
import scipy as sp
sys.path.insert(0, r"C:\Program Files\ANSYS Inc\v251\Lumerical\api\python")
sys.path.insert(0, r"C:\Users\PIC\Desktop\WeDaBest\LumOpt")
from lumopt.utilities.wavelengths import Wavelengths
from lumopt.geometries.polygon import FunctionDefinedPolygon
from lumopt.figures_of_merit.modematch import ModeMatch
from lumopt.optimizers.generic_optimizers import ScipyOptimizers
from lumopt.optimization import Optimization
# ---------- PARAMETERS ----------
R = 25e-6 # bend radius
W = 1.83e-6 # waveguide width
H = 1.0e-6 # waveguide thickness
n_bg = 1.44 # SiO2
n_ln = 2.20 # scalar LN approximation for optimization
wavelengths = Wavelengths(start=1550e-9, stop=1550e-9, points=1)
base_script = os.path.join(os.path.dirname(__file__), "base.lsf")
# ---------- OPTIMIZABLE 90 DEGREE BEND ----------
num_params = 8
theta_ctrl = np.linspace(-np.pi / 2, 0, num_params + 2)[1:-1]
initial_params = R * np.ones(num_params)
bounds = [(R - 4e-6, R + 4e-6)] * num_params
def bend_polygon(params=initial_params):
"""Return CCW polygon points for a variable-radius 90-degree bend."""
theta_all = np.concatenate(([-np.pi / 2], theta_ctrl, [0]))
r_all = np.concatenate(([R], params, [R]))
interp = sp.interpolate.interp1d(theta_all, r_all, kind="cubic")
theta = np.linspace(-np.pi / 2, 0, 160)
r = interp(theta)
r_outer = r + W / 2
r_inner = r - W / 2
# Circle center is at (0, R)
outer = np.column_stack((r_outer * np.cos(theta),
R + r_outer * np.sin(theta)))
inner = np.column_stack((r_inner * np.cos(theta[::-1]),
R + r_inner * np.sin(theta[::-1])))
points = np.vstack((outer, inner))
# force counter-clockwise orientation
x = points[:, 0]
y = points[:, 1]
area = 0.5 * np.sum(x * np.roll(y, -1) - y * np.roll(x, -1))
if area < 0:
points = points[::-1]
return points
geometry = FunctionDefinedPolygon(
func=bend_polygon,
initial_params=initial_params,
bounds=bounds,
z=0.5e-6,
depth=H,
eps_out=n_bg ** 2,
eps_in=n_ln ** 2,
edge_precision=5,
dx=1e-9
)
# ---------- FIGURE OF MERIT ----------
fom = ModeMatch(
monitor_name="fom",
mode_number=1,
direction="Forward",
multi_freq_src=False,
target_T_fwd=lambda wl: np.ones(wl.size),
norm_p=1
)
# ---------- OPTIMIZER ----------
optimizer = ScipyOptimizers(
max_iter=40,
method="L-BFGS-B",
scaling_factor=1e6,
pgtol=1e-9
)
# ---------- RUN ----------
opt = Optimization(
base_script=base_script,
wavelengths=wavelengths,
fom=fom,
geometry=geometry,
optimizer=optimizer,
use_var_fdtd=True,
hide_fdtd_cad=False,
use_deps=True
)
opt.init_plotter()
opt.plotter.movie = False
opt.run()

## Slide 15: 2nd Optimization Approach
Develop a better connection + segmented approach
  Instead of fixing the center of the radius in space we will vary it
  Optimizing the center line

## Slide 16: Centerline Design Conditions
Curvature always increasing
The derivative of the interface should not exceed a constant
  Otherwise decrease the merit function dramatically

## Slide 17: 2nd Optimization Results
Notes: Parameters
FINAL_PARAMETERS = np.array([
8, 8, 8, 8, 8, 8, 8, 8, 8, 8, 8, 8,
8, 8, 8, 8, 8, 8, 8, 8, 8, 8, 8, 8,
7.61722473, 8, 8, 7.15012409, 7.13035446, 7.28150568, 7.05481233, 7.01284343,
6.03618893, 5.65930189, 5.25973473, 5.42884294, 5.70837556, 4.34931513, 4.08031433, 3.77154924,
3.97284412, 3.19551698, 3.84706762, 2.87007739, 2.6051482, 3.30981182, 2.48654471, 1.58624323,
0.43604423, 1.58228282, 1.61901089, 1.64877403, 1.32884313, 0.20761352, 0.35015352, 1.79662236,
1.53864407, 0.66675978, -0.81190193, -0.89666845, 0.75307424, 0.69565405, -0.31614019, -0.71173202,
-0.09031953, 0.5942629, 0.86410944, 0.51041575, -0.37324764, -0.26461599, -0.22303369, 0.57406635,
1.60814363, 1.6465984, 1.2783256, 1.58787588, 0.47968965, 0.14519836, 1.67400531, 1.87038509,
1.68976327, 2.10630437, 2.18942169, 1.68427693, 2.61159037, 2.6765302, 3.02271604, 2.80814316,
2.81205414, 2.23836732, 3.63169119, 3.05323522, 3.38069699, 3.87437199, 4.12676747, 4.05052522,
4.35699329, 4.35016011, 4.5, 4.5
])

## Slide 18: 2nd Optimization Results
FOM = 0.012…
Loss
  Undermined
    Until the FDTD and Mode gets freed up
  Conclusion is not great >10 db losses

## Slide 19: Using FDTD Mode
Began using FDTD after simulating with the MODE viewer for prelim
  Conclusions
    Definitions of the components change from varFTDT to FTDT mode
      i.e. addmonintor

## Slide 20: Simulating Straight Waveguide (FDTD)
Using the following optimized parameters
0.9 um
0.3 um
70 degrees

## Slide 21: Simulating + Optimizing For Straight Waveguide
Performance
  0.04 db for 20 um …
    Good enough for testing our bent geometry
0.9 um
0.3 um
70 degrees
LN
SiO2
0.3 um
4.7 um

## Slide 22: FDTD With Bent Continuous Waveguide
Continuous bending radius
  10 um radius
Results
  0.0551955 dB

## Slide 23: varFDTD With Varying Bent Waveguide Structrue
NOTE: I attempted many different times to attain the same loss results with the varFDTD with the FDTD, but always got much worse results with MODE. I.e. this demonstrated to me that it is generally impossible for this geometry because of the 3D surface… Additionally when we changed the sidewall angle from 70 – 90 degrees we saw >10db difference. This demonstrated that MODE (varFDTD ) used for bent structures is not accurate.
Conclusion
  For more accurate simulation results FDTD mode is necessary

## Slide 24: FDTD With Bent Optimized Waveguide
Varying curvature + smoothing
Results
  Transmission = 0.0209516
  Loss dB = 16.7878
Notes: FINAL_PARAMETERS = np.array([
8, 8, 8, 8, 8, 8, 8, 8, 8, 8, 8, 8,
8, 8, 8, 8, 8, 8, 8, 8, 8, 8, 8, 8,
7.61722473, 8, 8, 7.15012409, 7.13035446, 7.28150568, 7.05481233, 7.01284343,
6.03618893, 5.65930189, 5.25973473, 5.42884294, 5.70837556, 4.34931513, 4.08031433, 3.77154924,
3.97284412, 3.19551698, 3.84706762, 2.87007739, 2.6051482, 3.30981182, 2.48654471, 1.58624323,
0.43604423, 1.58228282, 1.61901089, 1.64877403, 1.32884313, 0.20761352, 0.35015352, 1.79662236,
1.53864407, 0.66675978, -0.81190193, -0.89666845, 0.75307424, 0.69565405, -0.31614019, -0.71173202,
-0.09031953, 0.5942629, 0.86410944, 0.51041575, -0.37324764, -0.26461599, -0.22303369, 0.57406635,
1.60814363, 1.6465984, 1.2783256, 1.58787588, 0.47968965, 0.14519836, 1.67400531, 1.87038509,
1.68976327, 2.10630437, 2.18942169, 1.68427693, 2.61159037, 2.6765302, 3.02271604, 2.80814316,
2.81205414, 2.23836732, 3.63169119, 3.05323522, 3.38069699, 3.87437199, 4.12676747, 4.05052522,
4.35699329, 4.35016011, 4.5, 4.5
])

## Slide 25: Using FDTD In Detail
Notice
  Was taking 3 hours to simulate 50 um standard curve???
    Way too long
    Need a solution?

## Slide 26: Problem Solving
0.1um (step) | Full | Segmented
dB | 0.035909 | 0.035909
Time | 2 min | 15 s
0.05um (step) | Full | Segmented
dB | 0.114669 | 0.114669
Time | 20 min | 18 min
Decrease stepping size
Mesh override
  Low mesh res for the outside
  High mesh res for features of interest
    This method unfortunately is not viable because Lumeircal already performs non-uniform mesh optimization
    We do not see a significant speed up…